## Slide 1
Spiking vs. Standard PointNet
3-D Point Cloud Classification with Temporal Slicing & Early Exit
PointNet-SNN vs. PointNet-ANN on ModelNet10
Purdue Project — SNN Experiment
February 19, 2026
695K
Parameters
10
Epochs
ModelNet10
Dataset
16
Time Slices
1 / 14

## Slide 2
Outline
2 / 14
01
Motivation & Research Questions
02
Dataset — ModelNet10 & Radial Slicing
03
Model Architectures (ANN vs. SNN)
04
Training Setup & Loss Function
05
Training Results
06
Test Inference — 4 Modes
07
Accuracy vs. Timestep
08
Early Exit Analysis
09
Confidence Growth & Threshold Tradeoff
10
Analysis, Limitations & Next Steps
11
Conclusion

## Slide 3
Motivation & Research Questions
3 / 14
Why Spiking Neural Networks?
• Event-driven, sparse computation
• Biologically inspired temporal dynamics
• Energy-efficient on neuromorphic hardware
• Natural fit for sequential / streaming data
• Integrate-and-fire = running evidence accumulator
Research Questions
Q1
Can SNN-PointNet match standard ANN accuracy on ModelNet10 with the same training budget?
Q2
Does membrane potential accumulation across slices produce progressively better predictions?
Q3
Does confidence grow monotonically, enabling meaningful early exit at test time?

## Slide 4
Dataset — ModelNet10 & Radial Temporal Slicing
4 / 14
ModelNet10
Train samples
3,991
Test samples
908
Classes
10
Points per cloud (N)
1,024
Point features
(x, y, z) only
File format
.npy
10 Classes:
bathtub · bed · chair · desk · dresser monitor · night stand · sofa · table · toilet
Radial Temporal Slicing
1
Compute centroid mu = mean(points)
2
Compute radial distance d_i = ||p_i - mu||
3
Sort points inner -> outer by distance
4
Split into T=16 slices (64 pts / slice)
5
Feed slices sequentially to the network
Coarse-to-fine: inner slices = shape skeleton, outer slices = surface detail

## Slide 5
Model Architectures — ANN vs. SNN
5 / 14
Slice S_t [B, 64, 3]
->
Backbone MLP (per-point)
->
Mean Pool [B, 512]
->
Temporal Head (stateful)
->
Logits [B, 10]
Shared macro-architecture (695,562 parameters in both models)
PointNet-ANN (Baseline)
Backbone
3 x Linear + ReLU
3->128->256->512
Temporal head
2 x Linear + ReLU
512->512->512->10
State across slices
Cumulative mean
of slice embeddings
Activation
ReLU (standard)
f(x) = max(0,x)
Generalisation
76.2% test accuracy
(after 10 epochs)
PointNet-SNN (Proposed)
Backbone
3 x LIF layer
3->128->256->512
Temporal head
2 x LIF + FC
512->512->512->10
State across slices
Membrane potential
u_t = tau*u_(t-1)+Wx
Activation
Heaviside + surrogate
grad: 1/(1+|u|)^2
Generalisation
58.3% test accuracy
(after 10 epochs)

## Slide 6
LIF Neuron Dynamics & Training Loss
6 / 14
Leaky Integrate-and-Fire (LIF)
Membrane update:
u_t = tau * u_(t-1) + W * x_t
Spike emission:
s_t = Theta(u_t - theta)
Soft reset:
u_t <- u_t * (1 - s_t)
Surrogate grad:
ds/du ~ 1 / (1 + |u|)^2
Parameters
tau (decay)
0.9
theta (threshold)
1.0
Reset type
Soft (subtract)
Gradient approx.
Surrogate
Training Loss Function
L = L_CE(y_hat_T, y) + lambda * SUM L_CE(y_hat_t, y)
L_CE(y_hat_T, y)
Final-slice loss
Supervises the last timestep (T=16). Drives end-to-end accuracy.
lambda * SUM L_CE(y_hat_t, y)
Auxiliary loss (lambda=0.3)
Supervises ALL intermediate steps. Forces every slice to carry class information -> enables early exit.
Optimizer: AdamW | LR: 1e-3 | Grad clip: 1.0 | Batch: 16

## Slide 7
Training Results — 10 Epochs
7 / 14
Key Numbers
ANN Epoch 1
46.5%
ANN Epoch 10
83.2%
SNN Epoch 1
35.0%
SNN Epoch 10
87.4%
SNN starts slower (membrane calibration) but surpasses ANN by epoch 2
Both models converge stably with no spikes or instability.

## Slide 8
Test Inference — Four Evaluation Modes
8 / 14
ANN + Full
Test Accuracy
76.21%
Mean Exit Step
--- / 16
Single forward pass on all 1024 points. No slicing. Serves as the main baseline.
ANN + Slice
Test Accuracy
76.21%
Mean Exit Step
7.25 / 16
Cumulative mean of slice embeddings. Matches Full; exits at step 7 on average.
SNN + Full
Test Accuracy
9.25%
Mean Exit Step
--- / 16
Single pass, one membrane step. NOT the intended mode — near-random (temporal dynamics not engaged).
SNN + Slice
Test Accuracy
58.26%
Mean Exit Step
8.82 / 16
Sequential slices + persistent membrane. Intended SNN mode. Mean exit: step 8.82.
Why is SNN+Full near-random (9.25%)?
The SNN temporal head is designed to integrate across 16 slices, with membrane potential acting as a running accumulator. Feeding all 1024 points in ONE step gives only a single integration tick — the membrane never builds meaningful state. The correct comparison is SNN+Slice (58.3%).

## Slide 9
Accuracy vs. Timestep
9 / 14
Observations
ANN rises steeply, plateaus by slice 6-8
SNN shows slower but sustained growth
Both exceed baselines well before T=16
Early exit viable from slice 6 onward

## Slide 10
Early Exit Analysis
10 / 14
SNN exit histogram (theta = 0.80)
Cumulative exit distribution
ANN exits earlier on average (mean 7.25) vs. SNN (mean 8.82), reflecting faster confidence build-up via cumulative averaging. Both models allow substantial compute savings: at theta=0.80, roughly half the slices can be skipped on average without waiting for the final step.

## Slide 11
Confidence Growth & Threshold Tradeoff
11 / 14
Avg. max-softmax confidence per slice
Accuracy vs. mean exit step (theta sweep)
Confidence grows monotonically for both models — validating temporal slicing. The threshold curve (right) sweeps theta in [0.50, 0.99]: low theta gives early exit with lower accuracy; high theta defers to the final slice and recovers full accuracy. This tradeoff can be tuned at inference time with no retraining.

## Slide 12
Analysis & Limitations
12 / 14
Key Findings
✓
SNN achieves higher training acc (87.4%) than ANN (83.2%) in 10 epochs
✓
Test gap (ANN 76% vs SNN 58%) signals overfitting in the SNN
✓
Radial slicing enables early exit: ~45% avg compute savings at theta=0.80
✓
Confidence grows monotonically for both models — early exit is viable
✓
SNN+Full is invalid for this architecture (temporal dynamics not engaged)
Limitations
No GPU
Training on CPU only; 30+ epochs feasible with GPU in same time
Fixed LR
No schedule used; cosine/step decay expected to improve SNN generalisation
Small dataset
ModelNet10 has only 3991 train samples; ModelNet40/ScanObjectNN would stress-test more
No augmentation
Random rotation, jitter, scale would reduce overfitting significantly

## Slide 13
Recommended Next Steps
13 / 14
01 LR Scheduling
Cosine decay or step schedule; 30+ epoch training on GPU
02 Data Augmentation
Random rotation, jitter, scale; expected to close train-test gap
03 Regularisation
Dropout in temporal head; weight decay tuning for SNN
04 Learnable Thresholds
Per-layer adaptive LIF thresholds; learnable tau parameter
05 Larger Benchmarks
ModelNet40, ShapeNet, or ScanObjectNN for broader coverage
06 Energy Profiling
Measure spike rates and SynapticOps to quantify energy savings

## Slide 14
Conclusion
We presented a Spiking PointNet that processes 3-D point clouds as a temporal sequence of radial slices, enabling biologically motivated integrate-and-fire dynamics for 3-D shape classification.
SNN Train Acc
87.4%
Surpasses ANN training accuracy (83.2%)
ANN Test Acc
76.2%
Strong ANN baseline; gap to close with more training
SNN Test Acc
58.3%
Slice mode only; room to improve with regularisation
Early Exit
~45%
Avg compute savings at theta = 0.80
These results demonstrate the viability of spiking temporal processing for point cloud classification and motivate further work on GPU-accelerated, regularised SNN training for 3-D perception.
14 / 14